REQUEST FOR BID

Scott County Facility & Support Services is requesting quotations for Periodic Maintenance inspection on Boilers.  This service will be rendered one time per year, time to be agreed by vendor and Scott County.  Duration of contract will be from July 1, 2006 to June 30, 2008.

Bids should be submitted no later than 2:00 p.m. June 16, 2006 to the Scott County Purchasing Division, 428 Western Ave, Davenport, IA.  Quotations may be faxed, mailed or hand delivered (fax number is 563-326-8246).

The systems can be viewed by contacting Mark Kendall, Facility & Support Services, 563-326-8287for an appointment.

Maintenance inspections will include:

Boiler list is attached

A.  Chimney

1.  Perform flue gas analysis.

2.  Inspect for soot and corrosion.

B.  Relief Valve

1.  Perform try lever test for proper closing.

C.  Controls and Safety Limits

1.  Blow down low water fuel cut-off.

2.  Perform operations tests and assure proper settings and operations:

- operating control;

- high temperature safety limit;

- flame failure safety;

- High/low gas pressure cut-off;

- Ensure all safety devices, including those not specified here are in proper working order; verify operation.

D.  Burner Section

1.  Check flame composition and shape.

2.  Perform combustion and draft test.

3.  Inspect and clean nozzles, passages, and orifices.

4.  Adjust fuel/air mixture as necessary to optimize combustion efficiency and heat transfer.

5.  Check and clean pilot and igniters.

E.  Gas Train

1.  Check for proper operation of main and safety shutoff

Valves;

2.  Check for leaks and overall security;

3.  Assure all gas valve shutoffs operate and seal properly;

4.  Check gas pressure regulator setting;

F.  Gauges

1.  Check for accuracy and proper operation.

INSURANCE REQUIREMENTS

The Contractor shall have in force during the period of this contract, insurance as listed below:

A.	Bodily Injury and Property Damage Insurance:  The CONTRACTOR shall take out and maintain during this contract, bodily injury and property damage liability insurance under a comprehensive general form and automobile injury and property damage insurance under a comprehensive general form.

The required limits of this insurance shall not be less than:

General Liability:

Personal Injury - each person				$1,000,000

Personal Injury - each occurrence				$1,000,000

Personal injury - Aggregate					$1,000,000

Personal Damage - each occurrence including

Broadform Liability Extension				$1,000,000

Automobile Liability - Owner, Non-Owned and Hired

Vehicles:

Personal Injury - each person				$1,000,000

Personal Injury - each occurrence				$1,000,000

Personal Damage - each occurrence			$1,000,000

The above insurance shall cover the contractor's employees, the public and Scott County employees while in the buildings and on the grounds of Scott County.

B.	Certificates of Insurance:  The CONTRACTOR shall deliver to Facility & Support Services , Scott County Bi-Centennial Building, 428 Western Ave., Dav. Ia. 52801, certificates of insurance covering all above insurance in duplicate.  Such certificates shall provide ten days prior notice by registered mail of any material change in, or cancellation of this insurance.  CONTRACTOR shall maintain this coverage on a standard CGL form for the benefit of Owner and the general public throughout the term of this agreement, and if a carrier or policy is changed, CONTRACTOR shall provide Owner with a replacement Certificate of Insurance.

C.	Contractual Liability Insurance:  The CONTRACTOR shall take out and maintain during this contract, liability insurance.

D.	Products and Completed Operations Liability Insurance:  The CONTRACTOR shall also take out Products and Completed Operations Liability Insurance of limits not less than any of the above limits specified in these qualifications.

E.	Workmen's Compensation and Employer's Liability:

(1)	The CONTRACTOR shall maintain during this contract, the statutory workmen's compensation and employer's liability insurance for all his employees to be engaged in the maintenance work under the contract.

(2)	The amount of Employer's Liability Insurance shall not be less than One Million ($1,000,000).

INDEMNIFICATION

A.	To the fullest extent permitted by law, the CONTRACTOR shall indemnify and hold harmless the Owner and their agents and employees from and against all claims, damages, losses and expenses, including but not limited to attorney's fees, arising out of or resulting from the performance of the WORK, provided that any such claim damage, loss or expense (1) is attributed to bodily injury, sickness, disease or death or to injury to or destruction of tangible property (other than the WORK itself) including the loss of use resulting therefrom, and (2) is caused in whole or in part by any negligent act or omission of the CONTRACTOR and subcontractor, anyone directly or indirectly employed by any of them or anyone for whose acts any of them may be liable, regardless of whether or not it is caused in part by a party indemnified hereunder.  Such obligation shall not be construed to negate, abridge, or otherwise reduce and otherwise exist as to any party or person described in this paragraph.

- In any and all claims against the Owner or any of their agents or employees by any employee of the CONTRACTOR, any subcontractor, anyone directly or indirectly employed by any of them or anyone whose acts any of them may be liable, the indemnification obligation under this paragraph shall not be limited in any way by any limitation on the amount or type of damages, compensation or benefits payable by or for the CONTRACTOR or any subcontractor under workers' or workmen's compensation acts, disability benefit acts or other employee benefit acts.

- Scott County reserves the right to reject any or all bids or proposals submitted without cause.  Further, Scott County reserves the right to re-bid or re-solicit for proposals for this project at any time in the future.  By submitting a proposal or bid each CONTRACTOR acknowledges these rights and authorizes Scott County to exercise them should the situation warrant.

LIST OF MAINTAINED EQUIPMENT

COURTHOUSE – 416 W 4 St, Davenport

1  Raypack Domestic Hot Water Boiler

Administrative Center – 428 Western Ave, Davenport

1  Burnham Hot Water Boiler

Model #4FN.209-40-LB

1  Gordon-Piatt Gas-Fired Burner Assembly

3  Burnham Modular Boilers

3  Gas-Fired Burner Assemblies

1  Lochinvar Domestic Hot Water Boiler and storage tank

JAIL – 428 Ripley Ave, Davenport

1 Ajax Hot Water Boiler

Model #WGB-3750-D

1 Gas-Fired Burner Assembly

1 RBI Model #HW0630 Domestic Hot Water Boiler and Storage tank

PINE KNOLL – 2504 Telegraph Rd, Davenport

6 Burnham Modular Boilers

6 Gas-Fired Burner Assemblies

1 Raypack Domestic Hot Water boiler and storage tank

JAIL ANNEX – 4715 Tremont Ave, Davenport

- Lochinvar Domestic Water Boilers

- Trane Gas fired Forced Air Heating Units

- Reznor Roof Hung Units

PATROL HEADQUARTERS – 4715 Tremont Ave, Davenport

- Gas Fired Forced Air Furnace Units (Residential Syle)

WAREHOUSE – 4715 Tremont Ave, Davenport

5 Reznor Gas fired Roof Hung Units